## Slide 1
THE DIGITAL
TWIN HAT
Advanced Haptic Navigation System for the Visually Impaired
Hands-Free · Context-Aware · Intelligent
Prototype Research Project | Raspberry Pi 5 + ESP32-C6 | 2025

## Slide 2
PROJECT VISION
The Problem
Traditional walking sticks have real limitations:
Ground-level detection only
Misses head-level obstacles
Requires constant hand use
No context-awareness of movement speed
Static, non-adaptive sensing radius
The Solution
The Digital Twin Hat moves sensing to the head:
Hands-free ultrasonic detection
Head-level obstacle awareness
Dynamic speed-aware safety zones
Real-time sensor fusion (RPi 5 + ESP32)
Upgrade path to AI & haptic feedback
→

## Slide 3
HARDWARE STACK
Raspberry Pi 5
Central Brain
Complex data processing, sensor fusion, and future AI inference at the edge.
ESP32-C6
Comms & Low-Latency I/O
Handles real-time sensor polling and wireless communication via Wi-Fi 6.
HC-SR04
Ultrasonic Sensor
Measures front-facing obstacle distances with precision pings instead of taps.
MPU6050
6-Axis IMU
Tracks gait, walking speed, and head orientation for dynamic safety zones.
🔊 Feedback: Buzzer — proximity-triggered auditory alerts with dynamic intensity based on speed and distance

## Slide 4
CORE LOGIC & FEATURES
01
Dynamic Proximity
Threshold
Alert triggers when obstacle is within 50cm
Feedback
Sustained loud BEEP signals immediate stop
Vantage Point
Head-mounted for obstacle detection vs. floor-only sticks
02
Velocity-Aware Sensing
MPU6050 Integration
Calculates real-time walking speed
Dynamic Warning Zone
Faster walking = larger sensing buffer for reaction time
Smarter Than a Stick
Adapts to user behavior — static sticks cannot
03
Digital Twin Concept
Environment Mapping
Physical space converted to digital data streams
Ultrasonic vs. Tapping
Silent ultrasonic pings replace physical stick taps
Higher Vantage Point
Head-level detection catches obstacles sticks always miss

## Slide 5
FUTURE ROADMAP
v1.0
Current
v1.5
Haptics
v2.0
AI Vision
v3.0
Cloud
Phase 2 — Haptic Feedback
Replace buzzer alerts with vibration motors for a fully silent, tactile navigation experience. Reduces noise pollution and works in loud environments.
Phase 3 — AI Integration
Leverage the Raspberry Pi 5 for on-device object recognition. Distinguish between a wall, a person, or a vehicle — providing semantic context to the user.
Phase 4 — Cloud Connectivity
Use the ESP32-C6 Wi-Fi 6 capabilities for emergency location tracking, caregiver alerts, and telemetry data collection for research improvements.
From proof-of-concept to a fully autonomous, AI-powered wearable navigator